## Slide 1: Getting to know the nRF54L15
Hello World – App core +FLPR
Hello World running on App Core and FLPR nRF54L15
SESSION 1 : 8h30 – 10h00
Feb 2025
Alex Rawstorne
Alexander.rawstorne@nordicsemi.no

## Slide 2: Prerequisites
nRF Connect for Desktop with all tools installed
nRF SDK 2.9.0 installed with VSCode
Power Profiler 2
3 USB Cables – 2 x Micro USB and 1 x USBC Bring a hub if your laptop doesn’t have enough USB ports
nRF Connect SDK Fundamentals - Nordic Developer Academy
Optional:
  Bluetooth Low Energy Fundamentals - Nordic Developer Academy
  nRF Connect SDK Intermediate - Nordic Developer Academy
  Cellular IoT Fundamentals - Nordic Developer Academy
Notes: Toolchain manager for easily downloading SDK
Programmer for flashing kits, memory visualization
LTE Link Monitor, send AT commands, see LTE link quality, etc
Trace collector for modem traces
VS Code: easy to use, easy to configure and extend IDE for Nordic developers
  nRF Debug, Youtube videos for VS Code
nRF Connect for Mobile, Bluetooth LE
nRF Toolbox

## Slide 3: AGENDA
Session | Start | End | Tools | 
1 | 8h30 | 10h00 | nrf54L15DK | UART working on FLPR and Cortex M33
Break | 10h00 | 10h15 |  | 
2 | 10h15 | 11h45 | nrf54L15-DK/nRF52840-DK/ PPK2 | Build iBeacon application on 54L15 and 52840 and compare power consumption
Lunch | 11h45 | 12h30 |  | 
3 | 12h30 | 14h00 | nrf54L15-DK | Get 1.3" OLED Display operating on nrf54L15
Break | 14h00 | 14h15 |  | 
4 | 14h15 | 15h15 | nRF54L15-DK | Continue session 3 followed by Questions Sam
Q/A Close | 15h15 | 15h30 |  | 
Notes: Toolchain manager for easily downloading SDK
Programmer for flashing kits, memory visualization
LTE Link Monitor, send AT commands, see LTE link quality, etc
Trace collector for modem traces
VS Code: easy to use, easy to configure and extend IDE for Nordic developers
  nRF Debug, Youtube videos for VS Code
nRF Connect for Mobile, Bluetooth LE
nRF Toolbox

## Slide 4: Agenda Session 1 8h30-10h00
NRF Connect
    Board Configurator
    Direct Test Mode
    Power Profiler
    Programmer
    Bluetooth Low Energy
Hello World on nRF54L15-DK
Hello World on FLPR
2 Hello Worlds running simultaneously on FLPR and App Core

## Slide 5: Session1 : Tasks
Board Configurator
  Unbox nRF54L15-DK and nRF52840-DK
  Plug in nRF54L15-DK and run Board Configurator
  Adjust IO Voltage to 3V0
  Can you do the same for nRF52840?
Direct Test Mode
  Copy sample Direct Test Mode.
  Create a Build Configuration for nrf54l15dk/nrf54l15/cpuapp
  Flash build – open a serial terminal and run TX test on band 39

## Slide 6: Session1 : Tasks continued
Power Profiler
  Turn the DK off
  Go into Power Profiler in nrf Connect and connect to the PPK2
  Ensure the USB cable is plugged into the “USB Data/Power”
  Ensure the Power mode is set to “Ampere Meter” and turn “Enable power output” switch on.
  Connect the Power profiler to the nRF54L15DK by removing the jumper.
  Measure current draw Ch 17 0dB
  ENSURE IT’S THE RIGHT WAY AROUND

## Slide 7: Session1 : Tasks continued
Programmer
  Open Programmer
  Connect to nRF54L15-DK
  Load the hex file in ProjDirectory/build/zephyr/zephyr.hex
  Write the hex file to the DK
Bluetooth Low Energy
  Open Bluetooth Low Energy in nRFConnect
  Connect your nRF52840 and Scan
  Search for AlexsBLE
  Connect and discover Services

## Slide 8: Session1 : Hello World
Create a new application by copying sample hello_world
  Create a nrf54l15 build configuration (buildapp directory) and run it
  Observe terminal output on Serial console
  Save the workspace
Modify the sample to enable Logging
  Add to proj.conf
    CONFIG_LOG=y
    CONFIG_LOG_BACKEND=y
  Add to main.c
    #include <zephyr/logging/log.h>
    LOG_MODULE_REGISTER(main,LOG_LEVEL_DBG);
    LOG_INF("Hello World! %s", CONFIG_BOARD_TARGET);
    Rebuild and check all is working

## Slide 9: Session1 : Hello World contd
Custom config option
Create CONFIG_MY_MESSAGE=“Rutronik’s the best”
  Create a Kconfig in the root directory and add
    menu “Workshop”
    config MY_MESSAGE
    string “Nordic's the best”
    default “Hello World Custom”
    endmenu
    menu “Zephyr Kernel”
    source “Kconfig.zephyr”
    endmenu
  Add the string in LOG_INF with CONFIG_MY_MESSAGE and Pristine Build
  Create CONFIG_MY_MESSAGE=“Hello Nordicers” in proj.conf and rebuild

## Slide 10: Session1 : Hello World contd
  Hello World on APP Processor
    Observe current consumption on PPK2 (330uA)
    Go to the build Configuration and Add Snippet nordic-flpr, Rebuild, FLASH and observe current conumption
      Note the flash size difference in 1. and 2.
      Note the power consumption increase (1mA vs 330uA)
  Hello World on FLPR Processor
    Create another build configuration build_flpr
    Build for the flpr processor and flash
    Open another terminal and observe output on the FLPR core
  Hello World on both App and Flpr in One Build System
    Create another Directory hw2
    Copy hello_world to that directory and delete build directory
    Create three files kconfig.sysbuild, sysbuild.conf and sysbuild.cmake (If you want to cheat, you can find these files in C:\ncs\v2.9.0\zephyr\samples\sysbuild\hello_world)

## Slide 11: Session1 : Hello World contd
Create sysbuild.conf. Add the lines
  SB_CONFIG_REMOTE_BOARD="nrf54l15dk/nrf54l15/cpuflpr"
Add Extra CMAKE options in build configuration
  -Dhw2_SNIPPET=nordic-flpr
KConfig.sysbuild
  source "${ZEPHYR_BASE}/share/sysbuild/Kconfig“
  config REMOTE_BOARD
  string "The board used for remote target“

## Slide 12: Session1 : Hello World contd
sysbuild.cmake
  if("${SB_CONFIG_REMOTE_BOARD}" STREQUAL "") message(FATAL_ERROR "REMOTE_BOARD must be set to a valid board name")
  endif()
  ExternalZephyrProject_Add(
  APPLICATION remote
  SOURCE_DIR ${APP_DIR}/remote
  BOARD ${SB_CONFIG_REMOTE_BOARD}
  )
  set_property(GLOBAL APPEND PROPERTY PM_DOMAINS CPUFLPR)
  set_property(GLOBAL APPEND PROPERTY PM_CPUFLPR_IMAGES remote)
  set_property(GLOBAL PROPERTY DOMAIN_APP_CPUFLPR remote)
  set(CPUFLPR_PM_DOMAIN_DYNAMIC_PARTITION remote CACHE INTERNAL "")
  add_dependencies(${DEFAULT_IMAGE} remote)
  sysbuild_add_dependencies(FLASH ${DEFAULT_IMAGE} remote)
Build the project and flash.
Connect to the other COM Port to see FLPR messages

## Slide 13: Session1 : Hello World contd
Remove the LOG Messages in the main.c file and replace with printf
  Make sure you see the message on the FLPR
Extra task.
  Create your own src directory in remote with another main.c
  Modify CMAKELISTS.TXT in the remote to use the remote/src/main.c
  Get the Custom Kconfig working on FLPR

## Slide 14: Agenda Session 2 10h15-11h45
  Power Consumption benefits iBeacon
    iBeacon on nRF54L15-DK
    Add a scan response with unique name
    Observe Current consumption – floor current and 3 advertising channels
    Optimise power consumption and reobserve
    Deploy the same code to nRF52840-DK

## Slide 15: Session 2 Task
  Create a New Application
  Copy iBeacon Sample
    Create a Build Configuration for nrf54L15DK
    Add Scan Response data with a Name to advertising
      Add your device name CONFIG_BT_DEVICE_NAME="AlexBeacon"
      Define an array sd[] (look at beacon sample)
      Use the BT_DATA macro (NOT _BYTES) to add a custom name (FIELD,ID),
      Add scan response to the adv data () function
    Build, flash and find the device on Bluetooth Low energy and COM port
    Observe the floor current and Advertising with/without scan response
    Change the advertising interval to 1 second
      Inspect the variable BT_LE_ADV_NCONN
      Create BT_LE_ADV_CUSTOM
    Build, flash and then observe your device using Bluetooth Low Energy
    Measure current on the PPK2 and record it

## Slide 16: Session 2 Task
  Reduce the operational current by disabling LOG and the UART
      Hint, change the Settings in Proj.conf (SERIAL ? LOG ?)
      Measure the current on PPK2
  Reduce the average current to <7uA over a 10 sec interval
  Observe floor current
  Set transmit power to 8dB
    CONFIG_BT_CTLR_TX_PWR_PLUS_8
    CONFIG_BT_CTLR_TX_PWR_DYNAMIC_CONTROL
    CONFIG_MPSL_CALIBRATION_PERIOD=60000
  Record floor current and average over 10 sec at 1V8
  Record the same at 3V0
  Which is more efficient ?
Notes: 3uA at 3V, 3.6uA at 1V8 floor – Energy of floor is lower at 1v8
Max Tx 43.89uJ at 3V vs 43uJ for the TX current so pretty much the same
Averages – 29.16uJ at 3V vs 25.34uJ at 1.8V

## Slide 17: Session 2 Task
  Create a build configuration for nrf52840-DK
  Program at test it and measure floor and average current over 1min
  Compare nRF54L15 to nRF52840
  Which device wins the race ? Do it for 1.8V
Notes: 52840, 10.4uA
54L15, 9uA@3V, 13.7uA at 1.8

## Slide 18: Agenda Session 3 12h30-14h00
  Getting an 128 x 64 OLED Display working on nRF54L15-DK
    Block Diagram Architectural differences in nRF54L15
    Use the Display Driver in Zephyr
    Use the Character Frame buffer
    Use the LCD Driver for the SSH1106
  Setup the Device Tree for the Display
  Setup Proj.conf
  Use the drivers to display a message on the screen
  If there’s time use the LVGL driver library
  Get 2.42” display working on the kit

## Slide 19: nRF54L15 Block Diagram
To talk between ports you use the peripheral bridges. This takes time

## Slide 20: nRF54L15 Dedicated Clock pins

## Slide 21: Session3: Task
  Start with Beacon Example in Zephyr on nRF54L15-DK
  Add I2C OLED 128 x 64 Display
    Create an overlay file (disp54l.overlay)
    Modify the device tree to include i2c21
    Add Device Driver for sinowealth ssh1106
    Add Character Frame Buffer to the project
    Display “Hello”
  Repurpose the demo to the nRF54840-DK

## Slide 22: Port Pins on DK to connect Display to
Use P1 for the Connections
  Use P11 for SCL
  Use P10 for SDA
  Connect VDDIO to VCC on the Display
  Connect GND TO GND on the Display
  Ensure Power and GND are the correct way around as there are two different displays
  Use board configurator to set the Voltage to 3V

## Slide 23: Blinky and create an overlay file
Copy the sample Blinky and create a build configuration for nRF54L15
Create an overlay file – call it disp54l.overlay
  Add the i2c1 device
&i2c21 {
status = "okay";
zephyr,concat-buf-size=<1025>;
pinctrl-0 = <&i2c21_default>;
pinctrl-1 = <&i2c21_sleep>;
pinctrl-names = "default", "sleep";
};

## Slide 24: Blinky and create an overlay file
Pin Control – Define which pins do what
&pinctrl {
/omit-if-no-ref/ i2c21_default: i2c21_default {
group1 {
psels = <NRF_PSEL(TWIM_SDA, 1, 10)>,
<NRF_PSEL(TWIM_SCL, 1, 11)>;
};
};
/omit-if-no-ref/ i2c21_sleep: i2c21_sleep {
group1 {
psels = <NRF_PSEL(TWIM_SDA, 1, 10)>,
<NRF_PSEL(TWIM_SCL, 1, 11)>;
low-power-enable;
};
};
};

## Slide 25: Blinky and create an overlay file
Where do I find drivers ? Bindings index — Zephyr Project Documentation
Add the specifics of the sinowealth, ssh1106 in i2c21
sh1106_sh1106_128x64: ssd1106@3c {
compatible = "sinowealth,sh1106";
reg = <0x3c>;
width = <128>;
height = <64>;
segment-offset = <2>;
page-offset = <0>;
display-offset = <0>;
multiplex-ratio = <63>;
segment-remap;
com-invdir;
prechargep = <0x22>;
};
i2C Address 0x3C
Unique label that defines the display

## Slide 26: Blinky and create an overlay file
Link the driver to zephyr display and add the uart console
  / {
  chosen {
  zephyr,display = &sh1106_sh1106_128x64;
  zephyr,console = &uart20;
  };
  };
Build the application and make
sure there are no errors
Optional : Move the overlay to
the boards directory, rename it
to disp54l.overlay and explicitly
add it in the Extra Devicetree overlays section
The label you gave to the display
Link Uart20 to the zephyr console

## Slide 27: Blinky : Add drivers proj.conf
Edit proj.conf
  Enable the I2C driver
    CONFIG_I2C=y
  Enable Logging (So we can see if there is an I2C error)
    # Logging system
    CONFIG_LOG=y
    CONFIG_UART_CONSOLE=y
    CONFIG_I2C_LOG_LEVEL_DBG=y
  Enable I2C Driver
    # Display driver
    CONFIG_DISPLAY=y #Display driver
    CONFIG_HEAP_MEM_POOL_SIZE=4096 #Increase default heap siz
    CONFIG_CFB_LOG_LEVEL_DBG=y #Set Debug on for CFB
    CONFIG_CHARACTER_FRAMEBUFFER=y #Load CFB driver
    CONFIG_CHARACTER_FRAMEBUFFER_USE_DEFAULT_FONTS=y #Load default fonts

## Slide 28: Blinky : Add code to main.c
Build and Flash the application
  Connect the COMPort so you can see output
    Ensure there are no errors
    Disconnect SDA or SCK. Reboot and see if you get an error?
Modify main.c
  Include the zephyr/display/cfb.h
  Initialise the display
    struct device *display;
    display = (struct device *)DEVICE_DT_GET(DT_CHOSEN(zephyr_display));
    if (!device_is_ready(d->dev)) {LOG_ERR("Display not Present");return (1);}
  Refer to
    Zephyr API: Monochrome Character Framebuffer or
    https://docs.nordicsemi.com/bundle/zephyr-apis-2.8.0/page/group_monochrome_character_framebuffer.html

## Slide 29: Blinky : Add code to main.c
You need to
  Initialise the character frame buffer (init ?)
  Clear the CFB
  Print Hello on the display
  Try finalizing the frame buffer
  Read the number of fonts and try another font
  Invert the display
  Draw a line from 80,0 to 120,64
  Include the SHELL and CHARCTER_FRAMEBUFFER_SHELL
  Try (NOTE YOUR CODE SIZE DOWN)
    cfb scroll vertical 0 0 "Hello“
    cfb print 10 2 "Hello"

## Slide 30: Blinky : Get it running on 52840-DK
Create a device tree overlay for 52840DK
  Use i2c0
    P0.27 for SCL
    P0.26 for SDA
  Create a build configuration for nrf52840
Copy the project into another directory (lcd2BD)
  Modify the driver to SSD1306 and get the larger display running
  Take note Reset needs pulling high

## Slide 31: Blinky : LVGL Library (optional)
Goto LVGL — Light and Versatile Embedded Graphics Library
Copy your project to a LVGL directory
Add the LVGL driver
…